## Slide 1: Square-Root Coprocessor
Reconfigurable Computing
A FPGA Based Square-Root Approximation Coprocessor
Paulo Vasconcelos 84987
Pedro Teixeira 84715

## Slide 2: Theoretical Background

## Slide 3: Theoretical Background (I/III)
Goal: create a coprocessor to compute square root of non-negative integers
First approach: Newton's method
  Pros:
    Would allow for a configurable approximation order of magnitude;
    Recursive (easier to implement).
  Cons:
    Not exact result – even for square numbers;
    Composed of "not so easy to implement in hardware" operations (division);
    Problem with fractional values representation (floating vs fixed, single vs double precision).
Example: Square root of
  Initial iteration
  Iteration 1
  Iteration 2
  Iteration 3
  Iteration 4

## Slide 4: Theoretical Background (II/III)
Approach taken: Non-Restoring Algorithm
  Pros:
    Only integer values handled;
    Allows for a configurable word size;
    Mostly based on simple bitwise and shift operations;
    Recursive (with word size / 2 iterations).
  Cons:
    Unable to provide exact value for square root of non-perfect squares.
Figure 1 – Non-Restoring Algorithm

## Slide 5: Theoretical Background (III/III)
In the Non-Restoring Algorithm, the input value is processed times
  Since each iteration uses 2 bits of the input to produce 1 bit of the quotient output
The output is composed of two values:
  Quotient
    The approximate value of the square root of the number
    Equal to
  Remainder
    Difference to the closest (but inferior) square number
    Equal to
One can say:
Notes: Detected 1 CUDA Capable device(s) Device 0: "GeForce GTX 1060 6GB" CUDA Driver Version / Runtime Version 10.1 / 10.1 CUDA Capability Major/Minor version number: 6.1 Total amount of global memory: 5.93 GBytes (6372196352 bytes) GPU Clock rate: 1785 MHz (1.78 GHz) Memory Clock rate: 4004 Mhz Memory Bus Width: 192-bit L2 Cache Size: 1572864 bytes Max Texture Dimension Size (x,y,z) 1D=(131072), 2D=(131072,65536), 3D=(16384,16384,16384) Max Layered Texture Size (dim) x layers 1D=(32768) x 2048, 2D=(32768,32768) x 2048 Total amount of constant memory: 65536 bytes Total amount of shared memory per block: 49152 bytes Total number of registers available per block: 65536 Warp size: 32 Maximum number of threads per multiprocessor: 2048 Maximum number of threads per block: 1024 Maximum sizes of each dimension of a block: 1024 x 1024 x 64 Maximum sizes of each dimension of a grid: 2147483647 x 65535 x 65535 Maximum memory pitch: 2147483647 bytes

## Slide 6: Implemented Solution

## Slide 7: Basic Blocks & Architecture
Square Root Basic Block (SRBB)
  Defined a basic block responsible for 1 iteration of the Non-restoring algorithm
Square Root Block
  Defined a block responsible for replicating n/2 basic blocks and producing the results
Square Root Block
  A set of n/2 basic blocks in a chain produces the final result
    Used a for generate
    Used registers for a pipelined solution, decreasing the worst negative slack
  Inputs:
    CLK: the clock
    DATA_IN: the word
    NEW_VALUE: signalize a new valid word is being processed
  Outputs:
    SQRT: approximation for the Square Root value
    REMAINER: difference to the closest (but inferior) square number
    IS_SQUARE_NUM: indicates if a number is a square number
    DONE: indicates the output is valid
SquareRootBasicBlock
DATA_IN[31:0]
SQRT [31:0]
REMAINER [31:0]
IS_SQUARE_ROOT
SRB0
SquareRoot
SRBB1
…
SRBB n/2
CLK
NEW_VALUE
DONE

## Slide 8: Connecting the Coprocessor to the Hardware platform
Used the standard hardware platform
Having in mind the possible usage scenarios, a DMA based solution was used to connect to platform
  Avoiding the CPU to be responsible for each transfer between the memory and the peripheral
  Used a dedicated DMA mode
The coprocessor has 2 main interfaces:
Problem: The developed co-processor has, for 1 input, 2 outputs -> how to solve it?
  Multi channel DMAC (1 read channel, 2 write channels)
  2 DMAC
    Replication of logic! 
  Chosen solution -> use 1 DMAC and 1 output
    The length of the square root value will always be small or equal to n/2
    Remainer values greater than means the square root would be too imprecise -> codified those values with a special code indicating the square root approximation is not valid
Input word of bits
Output = bits for remainer + bits for the square root value

## Slide 9: Validating the solution

## Slide 10: Validating the Square Root Basic Block (for one iteration of the non-restoring algorithm)
Figure 2 – Results for testbench SquareRootBasicBlockTb
Each column of values correspond to different input values (i.e. no relation between set of values) No visible delays -> purely combinatory logic
Values for a non initial iteration of the algorithm
Value for an initial iteration of the algorithm

## Slide 11: Validating the Square Root Block (for all the iterations of the non-restoring algorithm)
Figure 3 – Results for testbench SquareRootBlockTb
First valid
value
Square Root Block is a synchronous block since it’s a pipelined set of Square Root Basic Blocks

## Slide 12: Timing & Performance Analysis

## Slide 13: Timing Analysis
Initial timing analysis
Final timing analysis
Critical path within the coprocessor slave interface (where the square root is computed)
Solved by adding bank of registers between each iteration (each SquareRootBasicBlock) turning a chain of combinatory blocks into a pipeline

## Slide 14: Performance Analysis
Figure 4 – Example of execution
Using random values with seed 243248
Other seed values can be used for obtaining different input pseudo-random values
Gains of times with the hardware version 